RAID Performance Analysis

We have six 500 GB disks with 8 ms average seek time. They rotate at 7200 RPM and have a transfer rate of 20 MB/sec. The minimum unit of transfer to each disk is a 512 byte sector. Assume the controller overhead is negligible. We want to compare three arrangements of these disks:

6 independent disks

6 disks arranged in RAID-1 (mirroring)

6 disks arranged in a RAID-5 (block-interleaved, rotated parity) with a block size of 0.5 MB

6 disks arranged in a RAID-6 (block-interleaved, rotated parity, 2 parity blocks per stripe) with a block size of 0.5 MB (data in stripe = 2 MB)

6 disks arranged in a RAID-10 (striping over mirroring) – block size of 0.5 MB over 3 logical drives (stripe = 1.5 MB), each logical drive made up of a mirrored pair

We will compare these arrangements for reads (large and small) and writes (large and small). Assume a small I/O is 512 bytes and a large I/O is 30MB (chosen so that it is evenly divisible by all 3 stripe sizes). For all answers, show your work.

- Capacity. (3 points) What is the minimum amount of real data we can store in each of these arrangements?

Table 1. Capacity

|  | Capacity (GB) |
| --- | --- |
| Independent Disks |  |
| RAID-1 |  |
| RAID-5 |  |
| RAID-6 |  |
| RAID-10 |  |

- Latency of Individual Operations. (15 points) Assume I/Os are distributed randomly, every I/O takes an average seek, and the disk does not reorder requests. You do not need to consider any queuing delays.

  - What is the total time to complete a small I/O operation on a single disk? (Note: It does not matter if it is a read or a write.)

  - What is the total time to complete a larges I/O operation on a single disk? (Note: It does not matter if it is a read or a write.)

  - Fill in the table with latencies for the specified configurations.

Table 2. Latency

|  | Small read (ms) | Small write (ms) | Large read (ms) | Large write (ms) |
| --- | --- | --- | --- | --- |
| Independent Disks |  |  |  |  |
| RAID-1 |  |  |  |  |
| RAID-5 |  |  |  |  |
| RAID-6 |  |  |  |  |
| RAID-10 |  |  |  |  |

- Throughput of Many Operations. (15 points) Compute the maximum number of I/Os per second for each request type. Assume individual I/Os on the same disk cannot be overlapped. In reality, writes would include time to compute new parity and would sometimes be destined for the same disk.

  - What is the maximum number of small I/Os per second for a single disk.

  - What is the maximum number of large I/Os per second for a single disk.

  - Fill in the table with maximum number of I/Os per second for the specified configurations. Whenever possible, assume that the independent requests do not conflict with one another (i.e. assume that they access different disks if possible.). Note: When there is more than one disk, throughput is rarely the inverse of latency because multiple operations can occur in parallel.

Table 3. Throughput

|  | Small read (IOs/sec) | Small write (IOs/sec) | Large read (IOs/sec) | Large write (IOs/sec) |
| --- | --- | --- | --- | --- |
| Independent Disks |  |  |  |  |
| RAID-1 |  |  |  |  |
| RAID-5 |  |  |  |  |
| RAID-6 |  |  |  |  |
| RAID-10 |  |  |  |  |

- Qualitatively how would answers in throughput table change if we did not make the assumption that independent requests do not conflict with each other?

- For which configurations are we less likely to get hot spots?

- Availability. (3 points) How many drives can fail in each configuration without data loss? Explain your answer.

Table 4. Availability

|  | Best Case: Maximum Number of Disks That Can Fail Without Data Loss | Worst Case: Minimum Number of Failed Drives Needed To Cause Data Loss |
| --- | --- | --- |
| Independent Disks |  |  |
| RAID-1 |  |  |
| RAID-5 |  |  |
| RAID-6 |  |  |
| RAID-10 |  |  |

- RAID5 Failure Case (5 points) For the following questions, describe in detail what happens in a RAID-5 system when one disk fails. You may assume a system with 6 disks.

  - ( 1 point) What happens when reading a piece of data from which the parity is stored on the failed disk?

  - (1 point) What happens when reading a piece of data for which the actual data is stored on the failed disk?

  - (1 point) If we replace the failed disk with a new disk, how could the system be returned to its original state?

  - (2 points) How much data would need to be read and written in during recovery? Estimate how long recovery would take if there were no competing requests in the system.

  - (2 points) What might happen if we want to write a new piece of data while there is still a failed disk in the system? List at least two options. For each option, say how this would complicate your answer to the previous question.

- Applications ( 3 points) Use the information in the preceding tables to recommend a configuration for the following workloads. Justify your answers.

  - Transaction Processing. This workload does a large number of small I/Os both reads and writes. Data integrity and availability is very important.

  - Personal home directories. These are typically stored on a file server. For file servers, capacity is important. Backups are done nightly.

  - Storage for video on demand. This workload is dominated by large reads. Availability and capacity are important.